## Slide 1: 2012 Beta Seminar
694 Software Engineering

## Slide 2: Overview
WPILib
  Command-based programming
  NetworkTables
  SmartDashboard
  Preferences
  Laptop-based vision processing
Jaguar firmware update
  Automatic Ramp mode
David dual relay module
4-slot cRIO-FRC II
Kinect

## Slide 3: Command-based Programming
Subsystems
  Define the capabilities of each part of the robot
  Subclasses of Subsystem
Commands
  Define the operation of the robot incorporating the capabilities defined in the subsystems
  Commands are subclasses of Command or CommandGroup

## Slide 4: Subsystems and Commands

## Slide 5: CommandGroup

## Slide 6: CommandGroup

## Slide 7: NetworkTables
Allow the programmer to easily send data between a laptop (either the driver station laptop or another laptop) and the robot
Applications
  SmartDashboard
  Preferences
  Laptop-based vision processing

## Slide 8: NetworkTables – Data Transfer
Bidirectional
  Robot can send data to a laptop
  Laptop can send data to robot
Named
  Key-value pairs
Full notification
  No need to poll for new values
  NetworkListener interface

## Slide 9: NetworkTables – Data Transfer
Multiple named tables
  e.g. SmartDashboard, Preferences
Transactional model
  Ensures that a group of values are updated simultaneously

## Slide 10: Preferences
Robot can save data such as constants in flash memory
Data can be accessed and modified using NetworkTable
Testing: IOException when trying to save

## Slide 11: Laptop-based Vision Processing
Vision processing requires heavy computation
Camera images can be processed on a laptop instead of on the cRIO
  NI Vision Library
  FIRST-provided Java wrapper for OpenCV (Open Source Computer Vision) library
    Documentation?
Data can then be sent back to robot using NetworkTable

## Slide 12: Jaguar - Firmware Update
Automatic Ramp mode
  694’s troubled relationship with Jaguars
  New Jaguar mode that, when activated, automatically ramps the output voltage to the motor at a preset ramp rate
  Can be accessed regardless of the control mode; Servo PWM, CAN, or Serial
One-second fan test

## Slide 13: Ramp Mode - Graph

## Slide 14: Ramp Mode - Jumpers

## Slide 15: Ramp Mode - Testing
Placed Mecanum drive robot on blocks
Set two Jaguars to normal mode and two to Automatic Ramp mode
Rapidly switched between full forward and full reverse using “button drive”
Two Jaguars failed; one on normal mode, and one on Automatic Ramp mode
  Became unresponsive, indicator LED not on
Jaguars operational after robot reboot

## Slide 16: David Dual Relay Module
Will not be available in 2012
Equivalent to two Spikes

## Slide 17: 4-slot cRIO-FRC II
team358.org

## Slide 18: 4-slot cRIO-FRC II — comparison
Single ethernet port
7” long (~2/3 the length)
30% lighter
256MB RAM (2x the old cRIO)
512MB storage (2x the old cRIO)

## Slide 19: Slot configuration (4-slot)
Slot “1”
Slot “2”

## Slide 20: Slot configuration (8-slot)
Slot “1”
Slot “2”

## Slide 21: How it works
cRIO determines the physical location of modules from code based on predetermined module order

## Slide 22: How it works
cRIO determines the physical location of modules from code based on predetermined module order
A Digital Module in slot “1” in code must be in physical cRIO slot 2

## Slide 23: How it works
cRIO determines the physical location of modules from code based on predetermined module order
A Digital Module in slot “1” in code must be in physical cRIO slot 2
A Digital Module in slot “2” in code must be in physical cRIO slot 4 on the 4-slot, and slot 5 on the 8-slot

## Slide 24: Huh?
Victor left_motor= new Victor(1, 5);
  Victor in 5th channel of Digital “1st” slot
    Physical Digital I/O slot #2 on both old & new cRIOs

## Slide 25: Huh?
Victor left_motor= new Victor(1, 5);
  Victor in 5th channel of Digital “1st” slot
    Physical Digital I/O slot #2 on both old & new cRIOs
Victor left_motor= new Victor(5);
  Same as above

## Slide 26: Huh?
Victor left_motor= new Victor(1, 5);
  Victor in 5th channel of Digital “1st” slot
    Physical Digital I/O slot #2 on both old & new cRIOs
Victor left_motor= new Victor(5);
  Same as above
Victor right_arm= new Victor(2,5);
  Victor in 5th channel of Digital “2nd” slot
    Physical Wildcard slot #4 on new cRIO
    Physical Digital I/O slot #6 on old cRIO

## Slide 27: Okay…
Gyro gyro = new Gyro(2, 1);

## Slide 28: Okay…
Gyro gyro = new Gyro(2, 1);
  Constructs a Gyro object in the 1st channel of the Analog “2nd” slot

## Slide 29: Okay…
Gyro gyro = new Gyro(2, 1);
  Constructs a Gyro object in the 1st channel of the Analog “2nd” slot
  Corresponds to physical 4th “wildcard” slot on new cRIO

## Slide 30: Okay…
Gyro gyro = new Gyro(2, 1);
  Constructs a Gyro object in the 1st channel of the Analog “2nd” slot
  Corresponds to physical 4th “wildcard” slot on new cRIO
  Corresponds to physical 5th Analog I/O slot on old cRIO

## Slide 31: Kinect

## Slide 32: Kinect
You are the joystick
Arms – “forwards” and “backwards”
Head, legs – “buttons”
Left Arm  left joystick
Right Arm  right joystick
Head/legs can be programmed to do anything

## Slide 33: Kinect
KinectStick left = new KinectStick(1);
KinectStick right = new KinectStick(2);
…
drivetrain.tankDrive(left, right);

## Slide 34: Kinect

## Slide 35: Thanks!
www.github.com/prog694
www.stuypulse.com